Eruptive Flux Rope Model Equations

---
Drag Force:
Gravitational Force:
Poloidal Field:
Inductance:
Toroidal Field:

---
Five Forces
- Internal JxB (Hoop Force)
- External JxB (Strapping Force)
- Drag Force
- Gravity Force
- Thermal Pressure Force

---
Five Forces
- Internal JxB (Hoop Force)
- External JxB (Strapping Force)
- Drag Force
- Gravity Force
- Thermal Pressure Force

---
Hoop Force
- Essentially it is a magnetic expansion force arising from magnetic pressure imbalance
- Strong, driving force initially that decreases as CME expands. Only positive force (for a fast CME)
- Both Major and Minor radius have hoop force component

---
External JxB
- Lorentz force caused by interaction between flux rope and overlying field, essentially magnetic drag force
- Can be fairly strong initially, but as ambient magnetic field begins to decrease, becomes less important
- Like gravity, it is important if you are concerned with CME initiation, not very important for CME propagation

---
Aerodynamic Drag Force
- The interaction between the flux rope and the solar wind that will accelerate/decline a CME to the solar wind speed
- It has long been our contention that the drag force is the most important force for CME propagation beyond the low corona
F_d=2 %rho v^2 c_d A

---
Matching Profiles to Measurements
For July 12, 2012 CME Flux rope arrival at 1 AU (~60 hours), duration (~24 hours)

---
Matching of profiles:
For now, focusing further out in the heliosphere (starting point between 20-30 Rs)

---
1 AU Comparison

---
- Why the ~80 km/s discrepancy in Velocity data? Comparing more of my measurements with in-situ data, drag model fittings match Bulk Speed, not Bulk+Expansion Speed
- The GCS model is measuring leading edge heights, so I expected expansion to be included
- This leads to an issue, as my measurements are allegedly along leading edge, but to match velocity expansion profile, drag velocity must be taken as central axis velocity
- How do I accurately compare?